## Slide 1: Geolocalizing Twitch Ingest Servers
LEE, HSIN-YUN 李昕耘
Network and Systems Laboratory
Graduate Institute of Electrical Engineering
National Taiwan University

## Slide 2: Outline
Introduction
Experiment Design
Packet Collection and RTT Measurement
Measurement Examination
Evaluate Experimental Results
Evaluate CBG - Shortest Distance Method
Conclusion

## Slide 3: Introduction
Motivation
Prior Geolocation Methods
Goal
Reference Point and Target
VPN
Twitch Ingest Server
Contribution

## Slide 4: Motivation
Importance of geolocalization
  Limit resource/information availability to specific regions
  Recommend different advertisement according to the region
  Provide a nearby CDN server for the user with less delay time
  Observe different online behaviors of people in different regions
  Track the footprints of Cybercrime

## Slide 5: Prior Geolocation Methods
  Check existing databases
    Verifies correspondence between [ip, geolocation] of DBs like MaxMind, NetAcuity
  Reverse DNS
    Use PTR record which stores the domain name corresponding to an IP to find the geolocation hint of an ip address
  Measurement-based geolocation
      Uses network latency to geolocalize target
        Shortest Ping - 2001
        GeoPing - 2001
        Constraint-Based Geolocation (CBG) - 2004
45.113.130.250
    video-edge-6ab7ae.tpe03.justin.tv
User
DNS Server

## Slide 6: Goal
Evaluate measurement–based geolocation methods
  Shortest Ping
  GeoPing
  Constraint-Based Geolocation (CBG)
  Need reference points and targets

## Slide 7: Reference Point and Target
Implement
Geolocation Methods
Reference Point = VP+LM
Target
Geolocalize
Evaluate the performance
probe
probe

## Slide 8
Widespread
Known location
Can actively probe other LMs or targets ➔ VP
Can be probed simply by ping ➔ LM
➔ Reference Points (VP + LM) = VPN
VPN

## Slide 9: VPN Distribution
There about 5000 VPN servers distributed on 82 locations for geolocalizing the target

## Slide 10: Twitch Ingest Server
Known location
Widespread
Allow streamers to upload live videos
➔ Target = Ingest Server
Streamer
Ingest Servers
Transcode
CDN Server
CDN Server
CDN Server
.
.
.
Streamer
Streamer
.
.
.
Upload
Distribute
Twitch live video delivery architecture
Viewer
Viewer
Viewer
Viewer

## Slide 11: Contribution
Provide VPN as a new tool for geolocation method
Discover additional usefulness of VPN
Evaluate the performance of these existing methods with VPNs as reference
Provide a hybrid geolocation method for evaluation
We can use the best geolocation method to geolocalize other unknown location target with VPN

## Slide 12: Experiment Design
Exploit VPN to Implement These Geolocation Methods
  Shortest ping
  GeoPing
  CBG
  Shortest Distance

## Slide 13: Exploit VPN to Implement These Geolocation Methods
Implement these geolocation methods by using VPN as VPs and LMs, and using twitch ingest servers as targets
  Shortest Ping
  GeoPing
  CBG
  Shortest Distance

## Slide 14: Shortest Ping
Calculate the RTT between each VP and the target
Map target to the VP location with the smallest RTT

## Slide 15
Calculate the RTT between all VP and a target to form a Target fingerprint
Calculate the RTT between all VP and a LM to form a LM fingerprint
  If a LM fingerprint is more similar to Target fingerprint ➔ map target to the LM location
GeoPing

## Slide 16: CBG
Calculate
Find the bestline “ ” with smallest total distance to all points “●”
Calculate to estimate
  ● e.g.
VP
RTT
① RTT
② Geo-Distance
Target
VP
Geo-Distance
Target
converted by bestline
5500 km
Target
VP: cr36
100 ms
Target
VP: cr36
VP
cr36
target
5500 km
VP: cr36
All LMs symbol “●”
Draw the circle
  VP’s location as center
  Estimated target distance as radius

## Slide 17: CBG
Map target to the LM’s location covered by the most circles e.g.
VP1
VP2
VP3
a
b
c
d
dist1
dist2
dist3
VP1 ➔ Bestline1 ➔ Estimated target dist1 ➔ Circle1
VP2 ➔ Bestline2 ➔ Estimated target dist2 ➔ Circle2
VP3 ➔ Bestline3 ➔ Estimated target dist3 ➔ Circle3
LM “a” is covered by the most circles
➔ Map target to LM “a” location

## Slide 18: Shortest Distance
After getting all estimated target distance from VPs by bestlines
Map the target to the VP location with smallest estimated distance.

## Slide 19: Packet Collection and RTT Measurement
These geolocation methods need the 3 RTTs
  Get Packet Transmission and RTT between
    NSLAB and VPN
    VPN and Twitch Ingest Server
    VPNs

## Slide 20: Packet Collection Architecture
NSLAB
Connect to VPN
VPN 82
.
.
.
Ingest 1
VPN 2
VPN 1
Ingest 2
Ingest 60
.
.
.
NSLAB
VPN 82
.
.
.
VPN 2
VPN 1
VPN 82 (LM)
.
.
.
VPN 2 (LM)
VPN 1 (LM)
Probe Ingests
Probe VPNs
NSLAB
VPN
①
①
①
②
③
②
To Get ②
To Get ③
Connect to VPN
Get ① + ②
Get ① + ③
Other 81 VPN (LM)
③
Ingest Server

## Slide 21: Get RTT1 between NSLAB and VPN
Packet Collection
  Ping each VPN from NSLAB
  Intercept the traffic
RTT Computation
  Take the minimum RTT in all pairs
NSLAB
VPN 82
.
.
.
VPN 2
VPN 1
ping
22:07:27.219059 IP 140.112.42.155 > 172.83.40.219: ICMP echo request, id 3, seq 16 ... 22:07:27.373360 IP 172.83.40.219 > 140.112.42.155: ICMP echo reply, id 3, seq 16 ...
RTT = 373.360 - 219.059
= 154.301 (ms)
VPN
VPN
NSLAB
NSLAB

## Slide 22: Get RTT2 between VPN and Twitch Ingest Server
Packet Collection
  Twitch ingest servers block ICMP packets
  Streaming on twitch to generate the traffic between VPN and ingest server
  Intercept traffic
NSLAB
Connect to VPN
VPN 82
.
.
.
Ingest 1
VPN 2
VPN 1
Ingest 2
Ingest 60
.
.
.
Streaming
RTT2

## Slide 23: Get RTT2 between VPN and Twitch Ingest Server
RTT Computation
  If seqnum(i) = acknum(j) ➔ pair packet(i) and packet(j)
  RTT = Time(j) – Time(i)
  Take the min RTT in all pairs = RTT1 + RTT2
  RTT2 = min RTT – RTT1
09:05:39.912347 IP 10.8.3.3.33882 > 52.223.218.164.1935: Flags [P.], seq 568718:569481 ...
…
09:05:39.986342 IP 52.223.218.164.1935 > 10.8.3.3.33882: Flags [.], ack 569481 ...
VPN
Ingest Server
VPN
Ingest Server
RTT = 986.342 - 912.347 = 73.995 (ms)
NSLAB
VPN
Ingest
RTT1
RTT2
Connect
Streaming
.
.
.
.
.
.
VPN 82
Ingest 60
Get RTT1+RTT2

## Slide 24: Get RTT3 between VPNs
Packet Collection
  Ping other 81 VPNs
  Intercept traffic
RTT Computation
  Take the min RTT in all pairs = RTT1 + RTT3
  RTT3 = min RTT – RTT1
NSLAB
VPN 82
.
.
.
VPN 2
VPN 1
VPN 82 (LM)
.
.
.
VPN 2 (LM)
VPN 1 (LM)
Connect
22:49:05.787483 IP 10.8.2.6 > 84.17.37.226: ICMP echo request, id 4, seq 39, length 64
22:49:06.122541 IP 84.17.37.226 > 10.8.2.6: ICMP echo reply, id 4, seq 39, length 64
ping
RTT3
RTT1
Get RTT1+RTT3

## Slide 25: Measurement Examination
RTT between NSLAB and VPN
RTT between VPN and Twitch Ingest Server
RTT between VPNs

## Slide 26: RTT1 between NSLAB and VPN
VPN | RTT(ms) | VPN | RTT(ms) | VPN | RTT(ms) | VPN | RTT(ms)
Taipei | 27 | Phoenix | 143 | Chisinau | 227 | Sofia | 263
Tokyo | 33 | Seattle | 151 | Warsaw | 229 | Steinsel | 263
Seoul | 52 | Salt Lake City | 158 | Vilnius | 231 | Tirana | 265
Hong Kong | 57 | Vancouver | 158 | Marseille | 232 | Sarajevo | 271
Kuala Lumpur | 72 | Denver | 163 | Milan | 233 | Tallinn | 272
Hanoi | 76 | Kansas City | 172 | Paris | 235 | Skopje | 272
Bangkok | 77 | Dallas | 172 | Riga | 235 | Reykjavik | 274
Singapore | 79 | Saint Louis | 186 | Brussels | 237 | Oslo | 276
Mumbai | 132 | Toronto | 190 | Frankfurt | 240 | Prague | 283
Istanbul | 249 | Chicago | 191 | Dublin | 243 | Ukraine | 283
Nicosia | 315 | Buffalo | 197 | London | 244 | Copenhagen | 285
Tel Aviv | 317 | Manassas | 198 | Amsterdam | 244 | Budapest | 286
Jakarta | 72 | New York | 198 | Lisbon | 245 | Athens | 289
Perth | 125 | Charlotte | 199 | Berlin | 246 | Helsinki | 290
Sydney | 131 | Montreal | 200 | Vienna | 251 | Stockholm | 296
Adelaide | 138 | Atlanta | 201 | Bratislava | 251 | Bucharest | 302
Melbourne | 141 | Miami | 203 | Madrid | 252 | Brazil | 310
Brisbane | 146 | Mexico | 195 | Zagreb | 254 | Tbilisi | 340
Auckland | 157 | San Jose | 263 | Ljubljana | 254 | Johannesburg | 372
Los Angeles | 130 | Santiago | 297 | Belgrade | 258 |  | 
San Francisco | 136 | Buenos Aires | 337 | Zurich | 263 |  | 
NSLAB
VPN
RTT1
Asia
Oceania
North America
South America
Europe
Africa
small
small
large

## Slide 27: RTT between NSLAB across VPN and Twitch Ingest Server
NSLAB
VPN
Ingest server
RTT1
RTT2
VPN
Ingest
 | Sydney | HK | Tokyo | Singapore | Copenhagen | Helsinki | London | Toronto | New York | Atlanta
Sydney | 132.103 | 254.181 | 295.18 | 223.025 | 389.237 | 394.846 | 376.974 | 375.431 | 382.195 | 312.87
HK | 218.907 | 23.535 | 73.56 | 55.603 | 275.262 | 290.616 | 216.386 | 209.839 | 225.084 | 220.447
Tokyo | 238.654 | 79.097 | 32.411 | 112.291 | 279.971 | 294.323 | 253.646 | 186.823 | 194.565 | 188.146
Singapore | 338.148 | 134.129 | 175.082 | 101.122 | 359.147 | 366.235 | 282.554 | 323.063 | 328.543 | 319.671
Copenhagen | 596.341 | 493.471 | 539.332 | 462.212 | 287.089 | 296.306 | 305.503 | 385.26 | 375.167 | 391.109
Helsinki | 616.653 | 529.269 | 536.325 | 454.795 | 282.18 | 274.17 | 298.439 | 367.873 | 357.72 | 374.585
London | 641.08 | 525.425 | 524.739 | 523.938 | 291.46 | 302.197 | 273.422 | 352.468 | 354.676 | 361.098
Toronto | 470.609 | 464.409 | 450.086 | 466.825 | 292.419 | 300.672 | 288.631 | 199.619 | 209.708 | 225.391
New York | 495.777 | 419.674 | 343.896 | 424.664 | 289.366 | 297.646 | 270.48 | 211.532 | 201.864 | 218.981
Atlanta | 479.777 | 458.404 | 435.509 | 448.14 | 307.378 | 317.794 | 296.766 | 227.145 | 221.98 | 201.424
Connected VPN
Ingest

## Slide 28: Unadjusted RTT2 between VPN and Twitch Ingest Server
VPN
Ingest server
RTT2
VPN
Ingest
 | Sydney | HK | Tokyo | Singapore | Copenhagen | Helsinki | London | Toronto | New York | Atlanta
Sydney | 1.103 | 123.181 | 164.18 | 92.025 | 258.237 | 263.846 | 245.974 | 244.431 | 251.195 | 181.87
HK | 161.907 | -33.465 | 16.56 | -1.397 | 218.262 | 233.616 | 159.386 | 152.839 | 168.084 | 163.447
Tokyo | 205.654 | 46.097 | -0.589 | 79.291 | 246.971 | 261.323 | 220.646 | 153.823 | 161.565 | 155.146
Singapore | 259.148 | 55.129 | 96.082 | 22.122 | 280.147 | 287.235 | 203.554 | 244.063 | 249.543 | 240.671
Copenhagen | 311.341 | 208.471 | 254.332 | 177.212 | 2.089 | 11.306 | 20.503 | 100.26 | 90.167 | 106.109
Helsinki | 326.653 | 239.269 | 246.325 | 164.795 | -7.82 | -15.83 | 8.439 | 77.873 | 67.72 | 84.585
London | 397.08 | 281.425 | 280.739 | 279.938 | 47.46 | 58.197 | 29.422 | 108.468 | 110.676 | 117.098
Toronto | 280.609 | 274.409 | 260.086 | 276.825 | 102.419 | 110.672 | 98.631 | 9.619 | 19.708 | 35.391
New York | 297.777 | 221.674 | 145.896 | 226.664 | 91.366 | 99.646 | 72.48 | 13.532 | 3.864 | 20.981
Atlanta | 278.777 | 257.404 | 234.509 | 247.14 | 106.378 | 116.794 | 95.766 | 26.145 | 20.98 | 0.424
Ingest
Connected VPN

## Slide 29: Adjust the RTT2 between VPN and Twitch Ingest Server
For each VPN, if there is a RTT between this VPN and an ingest server is minimum and < 0
  ➔ Each RTT between this VPN and each ingest server is subtracted by this RTT
Subtract -15.830
 | Sydney | Hong Kong | Tokyo | Singapore | Copenhagen | Helsinki | London | Toronto | New York | Atlanta
Helsinki | 326.653 | 239.269 | 246.325 | 164.795 | -7.820 | -15.830 | 8.439 | 77.873 | 67.720 | 84.585
VPN
Ingest
 | Sydney | Hong Kong | Tokyo | Singapore | Copenhagen | Helsinki | London | Toronto | New York | Atlanta
Helsinki | 342.483 | 255.099 | 262.155 | 180.625 | 8.010 | 0 | 24.269 | 93.703 | 83.550 | 100.415
VPN
Ingest

## Slide 30: Adjusted RTT2 between VPN and Twitch Ingest Server
RTT is very small if the VPN and ingest server are in the same city
RTT is small if the VPN and ingest server are in the same continent
is similar to in the same continent
VPN
Ingest server
Adjusted RTT2
 | Sydney | HK | Tokyo | Singapore | Copenhagen | Helsinki | London | Toronto | New York | Atlanta
Sydney | 1.103 | 123.181 | 164.18 | 92.025 | 258.237 | 263.846 | 245.974 | 244.431 | 251.195 | 181.87
HK | 195.372 | 0 | 50.025 | 32.068 | 251.727 | 267.081 | 192.851 | 186.304 | 201.549 | 196.912
Tokyo | 206.633 | 47.076 | 0.39 | 80.27 | 247.95 | 262.302 | 221.625 | 154.802 | 162.544 | 156.125
Singapore | 259.148 | 55.129 | 96.082 | 22.122 | 280.147 | 287.235 | 203.554 | 244.063 | 249.543 | 240.671
Copenhagen | 311.341 | 208.471 | 254.332 | 177.212 | 2.089 | 11.306 | 20.503 | 100.26 | 90.167 | 106.109
Helsinki | 342.483 | 255.099 | 262.155 | 180.625 | 8.01 | 0 | 24.269 | 93.703 | 83.55 | 100.415
London | 397.08 | 281.425 | 280.739 | 279.938 | 47.46 | 58.197 | 29.422 | 108.468 | 110.676 | 117.098
Toronto | 280.609 | 274.409 | 260.086 | 276.825 | 102.419 | 110.672 | 98.631 | 9.619 | 19.708 | 35.391
New York | 297.777 | 221.674 | 145.896 | 226.664 | 91.366 | 99.646 | 72.48 | 13.532 | 3.864 | 20.981
Atlanta | 284.676 | 263.303 | 240.408 | 253.039 | 112.277 | 122.693 | 101.665 | 32.044 | 26.879 | 6.323
Ingest
VPN A
Ingest B
RTT
VPN B
Ingest A
RTT
Connected VPN

## Slide 31: RTT3 between VPNs
 | Sydney | HK | Tokyo | Singapore | Copenhagen | Helsinki | London | Toronto | New York | Atlanta
Sydney | 0 | 122.204 | 99.093 | 92.21 | 256.181 | 322.814 | 253.441 | 188.256 | 194.397 | 184.645
HK | 123.033 | 0 | 47.197 | 32.196 | 246.841 | 311.243 | 238.894 | 222.636 | 199.757 | 215.802
Tokyo | 98.683 | 52.488 | 0 | 67.136 | 257.347 | 253.619 | 262.827 | 167.999 | 149.161 | 148.153
Singapore | 89.111 | 27.441 | 64.278 | 0 | 160.006 | 296.646 | 158.658 | 225.663 | 223.335 | 213.66
Copenhagen | 258.689 | 211.614 | 260.211 | 164.062 | 0 | 18.888 | 24.066 | 101.833 | 87.252 | 114.558
Helsinki | 307.33 | 254.472 | 248.76 | 301.343 | 0.866 | 0 | 17.486 | 100.532 | 85.356 | 99.915
London | 246.251 | 182.36 | 248.936 | 157.464 | 17.287 | 31.706 | 0 | 74.936 | 70.755 | 84.484
Toronto | 188.125 | 210.895 | 168.035 | 227.785 | 99.421 | 115.375 | 81.785 | 0 | 20.04 | 35.252
New York | 183.989 | 208.616 | 138.067 | 219.023 | 74.646 | 90.667 | 62.923 | 10.1 | 0 | 8.267
Atlanta | 234.989 | 201.367 | 135.265 | 206.119 | 92.839 | 102.305 | 77.483 | 22.181 | 7.992 | 0
VPN (LM)
Connected VPN
VPN
81 VPN (LM)
Adjusted RTT3
RTT is small if the two VPNs are in the same continent
is similar to in the same continent
Connected VPN A
VPN B (LM)
RTT
Connected VPN B
VPN A (LM)
RTT

## Slide 32: Evaluate Experimental Results
Evaluation Methodology
  Result of Target Mapping by Each Geolocation Methods
  Ground Truth
  Evaluation Parameter
    Rank Difference
    Error Distance
Evaluation Result

## Slide 33: Evaluation Methodology
Result of target mapping by each geolocation methods
Ground Truth
Ingest server (Target) | Corresponding VPN (Ground Truth)
Helsinki | Helsinki
London3 | London
London4 | London
Berlin | Berlin
Düsseldorf1 | Brussels / Amsterdam
Houston | Dallas
Toronto | Toronto
Singapore | Singapore
Seoul1 | Seoul
Ingest: Toronto |  | Shortest Ping |  | GeoPing |  | CBG |  | Shortest Dist
Mapping Priority | VPN | RTT (ms) | VPN | Eu_Dist | VPN | Covers (circles) | VPN | Estimated Dist­ (km)
1 | Toronto | 9.619 | Chicago | 223.660 | Toronto | 6 | Chicago | 703.764
2 | Chicago | 9.901 | Saint-Louis | 233.070 | Chicago | 5 | Toronto | 795.801
3 | Montreal | 11.994 | Miami | 240.357 | Manassas | 5 | Montreal | 855.075
4 | New York | 13.532 | Manassas | 248.048 | Buffalo | 5 | New York | 1170.576
5 | Manassas | 16.844 | Montreal | 250.196 | Montreal | 4 | Saint-Louis | 1285.269
6 | Saint-Louis | 17.364 | Buffalo | 254.543 | New York | 4 | Manassas | 1393.594
7 | Charlotte | 27.803 | Toronto | 260.993 | Saint-Louis | 3 | Charlotte | 2233.570

## Slide 34: Evaluation Parameter
Rank Difference
  If the mapping priority is k ➔ rank difference will be k-1
Error Distance
  Geo-distance between a mapped VPN geolocation and the Target’s ground truth location
Ingest: Toronto |  | Shortest Ping |  | GeoPing |  | CBG |  | Shortest Dist
Rank Different | VPN | RTT (ms) | VPN | Eu_Dist | VPN | Covers (circles) | VPN | Estimated Dist­ (km)
0 | Toronto | 9.619 | Chicago | 223.660 | Toronto | 6 | Chicago | 703.764
1 | Chicago | 9.901 | Saint-Louis | 233.070 | Chicago | 5 | Toronto | 795.801
2 | Montreal | 11.994 | Miami | 240.357 | Manassas | 5 | Montreal | 855.075
3 | New York | 13.532 | Manassas | 248.048 | Buffalo | 5 | New York | 1170.576
4 | Manassas | 16.844 | Montreal | 250.196 | Montreal | 4 | Saint-Louis | 1285.269
5 | Saint-Louis | 17.364 | Buffalo | 254.543 | New York | 4 | Manassas | 1393.594
6 | Charlotte | 27.803 | Toronto | 260.993 | Saint-Louis | 3 | Charlotte | 2233.570
Ingest: Toronto | Shortest Ping | GeoPing | CBG | Shortest Dist
Mapped VPN | Toronto | Chicago | Toronto | Chicago
Error Distance (km) | 0 | 701 | 0 | 701

## Slide 35: Evaluation Result
Rank 3 4 2 1 | Total error (km) 16249 48528 13139 12435
Rank 3 4 2 1

## Slide 36: Evaluate CBG - Shortest Distance Method
Introduction of CBG - Shortest Distance Method
Evaluation on Hybrid Method

## Slide 37
In each VPN:
  Circle Cover is more ➔ higher Cover Rank
  Estimated distance to target is smaller ➔ higher Short distance Rank
  Each rank give point_cover and point_dist to form a scaled score
  Look up the scaled score to convert the rank to point to get total point
  Map Target to the VPN location with highest total point
Target: Toronto ingest server
Scaled score
VPN | Circle Covers | Estimated dist
New York | 4 | 1170.576
Toronto | 6 | 795.801
Manassas | 5 | 1393.594
. | . | .
. | . | .
Rank | point_cover | point_dist
1 | 100 | 100
2 | 95 | 90
3 | 90 | 80
4 | 87 | 77
5 | 84 | 74
6 | 81 | 71
Introduction of Hybrid Method
VPN | Cover Rank | Short dist Rank
New York | 5 | 4
Toronto | 1 | 2
Manassas | 2 | 6
. | . | .
. | . | .
VPN | point_ cover | point_ dist | Total
New York | 84 | 77 | 161
Toronto | 100 | 90 | 190
Manassas | 95 | 71 | 166
. | . | . | .
. | . | . | .

## Slide 38: Evaluation on Hybrid Method
Rank 4 3 1 2 | Total error (km) 13139 12435 11608 12239
Rank 4 1 3 2

## Slide 39: Conclusion
The goal of this study is to evaluate the performance of existing geolocation methods that helps choose appropriate methods for future geolocalization
Among the four methods: Shortest Ping, GeoPing, CBG, and Shortest Distance, CBG method outperform than others
Hybrid method may lead to better performance which provides a hint for the development of future geolocation methods

## Slide 40: Q&A

## Slide 41: Get VPN Information
Use the command to get a json format VPN information curl --silent "https://api.nordvpn.com/v1/servers?limit=50000" | jq
"locations":
"id": 3984,
"created_at": "2018-06-18 14:45:14",
"updated_at": "2018-06-18 14:45:14",
"country":
"id": 108,
"name": "Japan",
"code": "JP",
"city":
  "id": 4633349,
  "name": "Tokyo",
  "latitude": 35.685,
  "longitude": 139.751389,
  "dns_name": "tokyo",
  "id": 963593,
  "created_at": "2020-06-09 10:37:53",
  "updated_at": "2022-04-13 17:44:24",
  "name": "Japan #556",
  "station": "89.187.161.144",
  "ipv6_station": "",
  "hostname": "jp556.nordvpn.com",
  "load": 21,
  "status": "online",

## Slide 42: Establish a VPN List
Codename | jp566
IP | 89.187.161.144
Country | Japan
City | Tokyo
Latitude | 35.685
Longitude | 139.751
VPN List:
Location 1: [latitude1], [longitude1], [Country1], [City1], [numbers of Servers1], [codename 1.1], [codename 1.2], [codename 1.3], ...
Location 2: [latitude2], [longitude2], [Country2], [City2], [numbers of Servers2], [codename 2.1], [codename 2.2], [codename 2.3], ...
  .
  .
  .

## Slide 43: VPN Selection
Select exactly one VPN for one location.
  R1: VPs perspectives are the same
  R2: LMs are also in the same location
  R3: Select at least one VPN from different locations to avoid wasting VPN resources
Location 1: [latitude1], [longitude1], [Country1], [City1], [numbers of Servers1], [codename 1.1], [codename 1.2], [codename 1.3], ...
Location 2: [latitude2], [longitude2], [Country2], [City2], [numbers of Servers2], [codename 2.1], [codename 2.2], [codename 2.3], ...
  .
  .
  .
Select exactly one VPN
Select exactly one VPN

## Slide 44: The Reason Why RTT May < 0
RTT1ping > RTT1connection + RTT2
  RTT2 is small ➔ imply VPN is close to ingest server
  RTT1ping : low priority ➔ more delay time
  RTT1connection : high priority ➔ less delay time
NSLAB
VPN
RTT1ping
NSLAB
VPN
Ingest server
RTT2
RTT1connection
NSLAB
VPN
After adjustment RTT1ping
Decrease RTT1ping
RTT1connection + RTT2 - RTT1ping = 0
=> RTT2 = 0

## Slide 45: Distribution of RTTmin
For each VPN, RTTmin = RTT1connection + RTT2 - RTT1ping
 | Sydney | HK | Tokyo | Singapore | Copenhagen | Helsinki | London | Toronto | New York | Atlanta
Helsinki | 326.653 | 239.269 | 246.325 | 164.795 | -7.820 | -15.830 | 8.439 | 77.873 | 67.720 | 84.585
VPN
Ingest
e.g. Minimum RTT between VPNHelsinki and all ingest servers is RTTmin = -15.830 ms
Helsinki
-15.830

## Slide 46: Evaluation Result on Rank Difference
Rank Diff. | Shortest Ping | GeoPing | Shortest Dist | CBG
0 | 40 | 22 | 40 | 40
1 | 5 | 11 | 8 | 7
2 | 2 | 7 | 2 | 3
3 | 2 | 3 | 0 | 1
4 | 1 | 3 | 0 | 1
5 | 0 | 2 | 0 | 3
6 | 0 | 2 | 2 | 1
7 | 0 | 2 | 1 | 0
8 | 2 | 1 | 0 | 1
9 | 0 | 1 | 0 | 2
≥ 10 | 8 | 6 | 7 | 1
Count the number of ground truth of each Rank Difference under each method
E.g. Shortest Ping have 40 ground truth in the first mapping priority , and 5 ground truth are ranked 2th priority of mapping

## Slide 47: Evaluation Result on Error Distance
Error Dist. | Shortest Ping | GeoPing | Shortest Dist | CBG
0 km | 40 | 22 | 40 | 40
50~100 | 1 | 0 | 1 | 0
100~200 | 3 | 0 | 3 | 4
200~300 | 0 | 0 | 0 | 0
300~400 | 5 | 5 | 5 | 3
400~500 | 0 | 2 | 0 | 4
500~600 | 2 | 2 | 1 | 1
600~700 | 0 | 2 | 0 | 0
700~800 | 1 | 6 | 2 | 2
800~900 | 2 | 2 | 2 | 2
900~1000 | 1 | 3 | 1 | 0
1000~1500 | 2 | 3 | 3 | 2
1500~2000 | 2 | 3 | 2 | 2
2000~3000 | 0 | 6 | 0 | 0
> 3000 km | 1 | 4 | 0 | 0
Count the number of mapped VPN of each Error Distance region under each method
E.g. Shortest Ping have 40 mapped VPN’s error distance are 0, and 3 mapped VPN’s error distance are located in 100~200 km

## Slide 48: Evaluation Result
Cumulative probability of rank difference (in %)
Rank Diff. | Shortest Ping | GeoPing | Shortest Dist | CBG
0 | 66 | 36 | 66 | 66
1 | 75 | 55 | 80 | 78
2 | 78 | 66 | 83 | 83
3 | 81 | 71 | 83 | 85
4 | 83 | 76 | 83 | 86
5 | 83 | 80 | 83 | 91
6 | 83 | 83 | 86 | 93
7 | 83 | 86 | 88 | 93
8 | 86 | 88 | 88 | 95
9 | 86 | 90 | 88 | 98
≥ 10 | 100 | 100 | 100 | 100
Error Dist. | Shortest Ping | GeoPing | Shortest Dist | CBG
0 km | 66 | 36 | 66 | 66
50~100 | 68 | 36 | 68 | 66
100~200 | 73 | 36 | 73 | 73
200~300 | 73 | 36 | 73 | 73
300~400 | 81 | 45 | 81 | 78
400~500 | 81 | 48 | 81 | 85
500~600 | 85 | 51 | 83 | 86
600~700 | 85 | 55 | 83 | 86
700~800 | 86 | 65 | 86 | 90
800~900 | 90 | 68 | 90 | 93
900~1000 | 91 | 73 | 91 | 93
1000~1500 | 95 | 78 | 96 | 96
1500~2000 | 98 | 83 | 100 | 100
2000~3000 | 98 | 93 | 100 | 100
> 3000 km | 100 | 100 | 100 | 100
Total err(km) | 16249 | 48528 | 13139 | 12435
Cumulative probability error distance (in %)

## Slide 49: Evaluation on Hybrid Method
Rank Diff. | Shortest Dist | CBG | Hybrid1 | Hybrid2
0 | 66 | 66 | 68 | 65
1 | 80 | 78 | 78 | 80
2 | 83 | 83 | 81 | 81
3 | 83 | 85 | 83 | 85
4 | 83 | 86 | 86 | 88
5 | 83 | 91 | 90 | 88
6 | 86 | 93 | 93 | 93
7 | 88 | 93 | 93 | 93
8 | 88 | 95 | 93 | 93
9 | 88 | 98 | 93 | 93
≥ 10 | 100 | 100 | 100 | 100
Cumulative probability of rank difference (in %)
Error Dist. | Shortest Dist | CBG | Hybrid1 | Hybrid2
0 km | 66 | 66 | 68 | 65
50~100 | 68 | 66 | 68 | 66
100~200 | 73 | 73 | 73 | 71
200~300 | 73 | 73 | 73 | 71
300~400 | 81 | 78 | 83 | 83
400~500 | 81 | 85 | 86 | 85
500~600 | 83 | 86 | 86 | 85
600~700 | 83 | 86 | 86 | 85
700~800 | 86 | 90 | 90 | 90
800~900 | 90 | 93 | 93 | 93
900~1000 | 91 | 93 | 93 | 93
1000~1500 | 96 | 96 | 96 | 96
1500~2000 | 100 | 100 | 100 | 100
2000~3000 | 100 | 100 | 100 | 100
> 3000 km | 100 | 100 | 100 | 100
Total err(km) | 13139 | 12435 | 11608 | 12239
Cumulative probability error distance (in %)

## Slide 50: Why GeoPing perform Poorly